## Slide 1
CodeChix Confidential Proprietary
15 Jan 2015
OFconnect
An OpenFlow SDN Library For Everyone
Deepa Karnad Dhurka
Ramya Bolla

## Slide 2: Agenda
Introduction
OFconnect Design
Unit Test Automation
Controller Integration
SDN Setup
Get Started!
15 Jan 2015 CodeChix.org OFconnect

## Slide 3: Software Defined Network
15 Jan 2015 CodeChix.org OFconnect
Source: opennetworking.org
  The physical separation of the network control plane from the forwarding plane, and where a control plane controls several devices.

## Slide 4: OpenFlow Channel Library
OpenFlow Channel Library
CONTROLLER
SWITCH
OpenFlow Protocol Connection
15 Jan 2015 CodeChix.org OFconnect
Problem
Duplication
High coupling with Controller/Switch
Poor multi version support
Solution
Abstract out OF Channel
Support Controller & Switch
Package into a library
Open Source it!

## Slide 5: Features
Hides wire protocol
Manages OF connections
Multi-language bindings
Platform independence
Functional
Other
15 Jan 2015 CodeChix.org OFconnect

## Slide 6: Next Up
Introduction
OFconnect Design
Unit Test Automation
Controller Integration
SDN Setup
Get Started!
15 Jan 2015 CodeChix.org OFconnect

## Slide 7: Design Goals
Performance under scale
        256K socket connections
Simultaneous multiple Transport Protocols
        TCP, UDP, TLS etc..
Easy addition of new Transport Protocols
Common API for controller & switch
15 Jan 2015 CodeChix.org OFconnect

## Slide 8: Scalability
TCP Datapath OFChannel (dpID:1, auxID:0)
UDP Auxiliary OFChannel (dpID:1, auxID:1)
UDP Auxiliary OFChannel (dpID:1, auxID:n)
TCP Datapath OFChannel (dpID:2, auxID:0)
UDP Auxiliary OFChannel (dpID:2, auxID:1)
UDP Auxiliary OFChannel (dpID:2, auxID:n)
TCP Datapath OFChannel (dpID:n, auxID:0)
UDP Auxiliary OFChannel (dpID:n, auxID:1)
UDP Auxiliary OFChannel (dpID:n, auxID:n)
Performance under scale
Controller is capable of handling 256K connections
15 Jan 2015 CodeChix.org OFconnect

## Slide 9: Block Diagram
Net Services
TCP, UDP etc.
Thread Mgr
Poll Thread Util
Elastic Pool
OFconnect API
Swig Bindings
Java, Python etc.
Controller/Switch
15 Jan 2015 CodeChix.org OFconnect

## Slide 10: OFconnect API
Net Services
TCP, UDP etc.
Thread Mgr
Poll Thread Util
Elastic Pool
OFconnect API
Swig Bindings
Java, Python etc.
Controller/Switch
15 Jan 2015 CodeChix.org OFconnect

## Slide 11: cc_of_lib.h
cc_of_ret cc_of_lib_init
cc_of_ret
cc_of_lib_free
cc_of_ret cc_of_dev_register
cc_of_ret cc_of_dev_free
cc_of_ret cc_of_send_pkt
typedef int (*cc_of_recv_pkt)
cc_of_ret cc_of_create_channel
cc_of_ret cc_of_destroy_channel
typedef int (*cc_of_accept_channel)
typedef int (*cc_of_delete_channel)
15 Jan 2015 CodeChix.org OFconnect
Initialize
OF Channel Setup
Tx/Rx

## Slide 12: OF Channel Setup
15 Jan 2015 CodeChix.org OFconnect

## Slide 13: OF Channel Setup Logs
15 Jan 2015 CodeChix.org OFconnect
ubuntu:~/deepa-git/mul-OFconnect/mul$ sudo ./mul
cc_onf_driver_lib-INFO: cc_of_lib_init(57): CC_OF_LIB Started Initializing
(process:7827): cc_onf_driver_lib-DEBUG: cc_of_lib_init(120): CREATED POLLTHR FOR listen sockets
(process:7827): cc_onf_driver_lib-DEBUG: cc_of_lib_init(131): CREATED POLLTHR FOR rwsockets
cc_onf_driver_lib-INFO: cc_of_lib_init(133): CC_OF_LIB initilaized successfully
cc_onf_driver_lib-INFO: cc_of_dev_register(232): Started Registering new Device
(process:7827): cc_onf_driver_lib-DEBUG: cc_of_dev_register(290): actual key returned 0x7f000001 ip address
(process:7827): cc_onf_driver_lib-DEBUG: fd: 10 fd_type: 0 pollin_func: 0x7f875cfb07ab pollout_func: (nil) events: 1
(process:7827): cc_onf_driver_lib-DEBUG: cc_of_dev_register(308): Created TCP listenfd
cc_onf_driver_lib-INFO: cc_of_dev_register(332):CC_OF_DEV initilaized successfullywith controllerIp:1.0.0.127, siwtchIp:0.0.0.0, controllerL4Port:6633
2015/01/04 16:56:48 MUL-CONTROLLER: (c_alloc_thread_ctx) nthreads:0
2015/01/04 16:56:48 MUL-CONTROLLER: c_thread_event_loop: tid(1523967744)
2015/01/04 16:56:48 MUL-CONTROLLER: c_thread_event_loop: tid(1515575040)
2015/01/04 16:56:48 MUL-CONTROLLER: c_main_thread_final_init: running tid(1532360448)
2015/01/04 16:56:48 MUL-CONTROLLER: (mul_cc_thread_event_loop_lib_support) tid(1532360448)
2015/01/04 16:56:48 MUL-CONTROLLER: mul-vty app registered
2015/01/04 16:56:48 MUL-CONTROLLER: VTY THREAD RUNNING
2015/01/04 16:56:53 unknown: Vty connection from 127.0.0.1
==== start mininet ====
2015/01/04 16:57:38 MUL-CONTROLLER: (mul_cc_of_accept) Accept received dpid:31 auxid:0x1f
2015/01/04 16:57:38 MUL-CONTROLLER: (mul_cc_of_accept) New switch context created
2015/01/04 16:57:38 MUL-CONTROLLER: (mul_cc_of_accept) switch:port str:127.0.0.1:49879
2015/01/04 16:57:38 MUL-CONTROLLER: (of_switch_add) Added to the hashtable dpid:31
2015/01/04 16:57:38 MUL-CONTROLLER: (of_send_hello) Send Hello to library dummy_dpid:31
2015/01/04 16:57:38 MUL-CONTROLLER: (c_thread_tx) Sending packet to library 31

## Slide 14: Net Services
Net Services
TCP, UDP etc.
Thread Mgr
Poll Thread Util
Elastic Pool
OFconnect API
Swig Bindings
Java, Python etc.
Controller/Switch
15 Jan 2015 CodeChix.org OFconnect

## Slide 15: Net Services Callbacks
typedef struct net_svcs_ {
int (*open_clientfd) (..);
int (*open_serverfd) (..);
int (*accept_conn) (..);
int (*close_conn) (..);
ssize_t (*read_data) (..);
ssize_t (*write_data) (..);
} net_svcs_t;
net_svcs_t tcp_sockfns = {
tcp_open_clientfd,
tcp_open_listenfd,
tcp_accept,
tcp_close,
tcp_read,
tcp_write,
};
Callbacks
TCP Registration
15 Jan 2015 CodeChix.org OFconnect

## Slide 16: HOWTO Add L4 Proto
Enumerate the new protocol: L4_type_e
Define NET_SVCS callback functions
Define socket POLL-IN/POLL-OUT callbacks
15 Jan 2015 CodeChix.org OFconnect

## Slide 17: TCP Net Services Logs
15 Jan 2015 CodeChix.org OFconnect
ubuntu:~/deepa-git/mul-OFconnect/mul$ sudo ./mul
2015/01/04 16:56:53 unknown: Vty connection from 127.0.0.1
==== start mininet: channel setup ====
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(401)[oflisten_thr]: POLLIN on fd 12
(process:7827): cc_onf_driver_lib-DEBUG: process_listenfd_pollin_func(92):, Calling netsvcs Accept, dev_key->ControllerIP 2130706433, dev_key->SwitchIp 0
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(401)[rwthr_1]: POLLIN on fd 8
(process:7827): cc_onf_driver_lib-DEBUG: pollthr_pri_pipe_process_func(507)[rwthr_1]: message received: fd type: 1, fd 31, fd action 0, poll events 5, in func: 0x7f875cfb1f9f, out func: 0x7f875cfb2b71
(process:7827): cc_onf_driver_lib-DEBUG: tcp_accept(474): client_ip:16777343 port:49879
2015/01/04 16:57:38 MUL-CONTROLLER: (mul_cc_of_accept) Accept received dpid:31 auxid:0x1f
(process:7827): cc_onf_driver_lib-DEBUG: tcp_accept(502): Updated TCP channel State to CC_OF_RW_UP
=== rx/tx ====
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(401)[rwthr_1]: POLLIN on fd 31
(process:7827): cc_onf_driver_lib-DEBUG: tcp_read(516): Receiving from socket 31
(process:7827): cc_onf_driver_lib-DEBUG: process_tcpfd_pollin_func(225)[rwthr_1]: Read a pkt on tcp sockfd: 31, dp_id: 31, aux_id: 31and sent it to controller/switch
2015/01/04 16:57:38 MUL-CONTROLLER: (of_send_hello) Send Hello to library dummy_dpid:31
2015/01/04 16:57:38 MUL-CONTROLLER: (c_thread_tx) Sending packet to library 31
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(412)[rwthr_1]: POLLOUT on fd 31
(process:7827): cc_onf_driver_lib-DEBUG: process_tcpfd_pollout_func(260)[rwthr_1]: Sent a pkt out on tcp sockfd: 31

## Slide 18: Block Diagram
Net Services
TCP, UDP etc.
Thread Mgr
Poll Thread Util
Elastic Pool
OFconnect API
Swig Bindings
Java, Python etc.
Controller/Switch
15 Jan 2015 CodeChix.org OFconnect

## Slide 19: Thread Management
Thread mgr
Poll-thread Util
Thread Admin Block
15 Jan 2015 CodeChix.org OFconnect

## Slide 20: Inside A Thread
OFconnect
API Tx
Net Services Protocol Callbacks
Poll Loop
Add/Del FD's
Control Pipe
Data Pipe
Pkt Send
POLL IN/OUT
POLL IN/OUT
POLL IN/OUT
15 Jan 2015 CodeChix.org OFconnect
Net Services Pollin/Pollout Callbacks
OFconnect
API Rx

## Slide 21: Elastic Pool
Thread Mgr
Poll Thread Util
Thread Mgr
Poll Thread Util
Elastic Pool
Block 1
Block 2
Block n
15 Jan 2015 CodeChix.org OFconnect

## Slide 22: Elastic Pool
Global ofrw_pollthr_list
  Sorted: decreasing no. of available sockets
cc_find_or_create_rw_pollthr_safe()
  Iterates to the last thread with availability
15 Jan 2015 CodeChix.org OFconnect

## Slide 23: Elastic Pool
cc_add_sockfd_rw_pollthr_safe()
  Calls cc_find_or_create_rw_pollthr_safe()
  Adds socket fd to rw pollthread
cc_del_sockfd_rw_pollthr_lockfree()
      Deletes socket from thread
      Sorts the list
15 Jan 2015 CodeChix.org OFconnect

## Slide 24: Thread Manager Logs
15 Jan 2015 CodeChix.org OFconnect
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(401)[rwthr_1]: POLLIN on fd 10
(process:7827): cc_onf_driver_lib-DEBUG: pollthr_data_pipe_process_func(673)[rwthr_1]: message received: size: 32, fd : 31
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(412)[rwthr_1]: POLLOUT on fd 32
(process:7827): cc_onf_driver_lib-DEBUG: process_tcpfd_pollout_func(260)[rwthr_1]: Sent a pkt out on tcp sockfd: 32
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(460)[rwthr_1]: Resetting POLLOUT flag for fd 32
(process:7827): cc_onf_driver_lib-DEBUG: adp_thr_mgr_poll_thread_func(866)[rwthr_1]: listing 4 items of updated pollfd_arr
(process:7827): cc_onf_driver_lib-DEBUG: adp_thr_mgr_poll_thread_func(875)[rwthr_1]: thr_pvt_p->pollfd_arr[0].fd: 8
(process:7827): cc_onf_driver_lib-DEBUG: adp_thr_mgr_poll_thread_func(875)[rwthr_1]: thr_pvt_p->pollfd_arr[1].fd: 10
(process:7827): cc_onf_driver_lib-DEBUG: adp_thr_mgr_poll_thread_func(875)[rwthr_1]: thr_pvt_p->pollfd_arr[2].fd: 31 (process:7827): cc_onf_driver_lib-DEBUG: adp_thr_mgr_poll_thread_func(875)[rwthr_1]: thr_pvt_p->pollfd_arr[3].fd: 32 (process:7827): cc_onf_driver_lib-DEBUG: adp_thr_mgr_poll_thread_func(813)[rwthr_1] before poll
(process:7827): cc_onf_driver_lib-DEBUG: poll_fd_process(401)[rwthr_1]: POLLIN on fd 32
(process:7827): cc_onf_driver_lib-DEBUG: tcp_read(518): Received 176 bytes from socket 32
(process:7827): cc_onf_driver_lib-DEBUG: process_tcpfd_pollin_func(144): RECEIVED PKT LENGTH IS 176 on channel dp_id-32 aux_id-32
(process:7827): cc_onf_driver_lib-DEBUG: process_tcpfd_pollin_func(157)[rwthr_1]: Received a message \u0001\u0006
2015/01/04 16:57:39 MUL-CONTROLLER: (mul_cc_recv_pkt) Recv received dpid:32 auxid:32 msg_len:176
Poll-in
Poll-out

## Slide 25: Next Up
Introduction
OFconnect Design
Unit Test Automation
Controller Integration
SDN Setup
Get Started!
15 Jan 2015 CodeChix.org OFconnect

## Slide 26: gtester
Two ways to run tests
  make runtest OR
  gtester --verbose -o=<log.xml> -k <test.exe>
Coverage
      cc_pollthr_mgr.c – 100%
      cc_of_util.c – approx. 75%
      cc_tcp_conn.c – approx. 80%
15 Jan 2015 CodeChix.org OFconnect
Notes: pollthr_test.c
pollthread_tc_1 Basic health of single pollthread upon bringup and tear down
Test Primary Pipe and Data Pipe
Test Self-Destruct of pollthread
Test add and delete of FDs
pollthread_tc_2 Addition/Deletion of new pipe(s)
Test pipe creation and addition to the pollthread
Test pollin function on the new pipe
Test deletion of pipe(s)
pollthread_tc_3 Exercise receive path of data - POLLIN on socket
Test socket addition to the poll loop with unix sockets
Test pollin function to test receive of packet
Delete the socket from pollthread
pollthread_tc_4 Exercise send path of data - POLLOUT on socket
Test socket addition to the poll loop with unix sockets
Test pollout function to test transmit of packet
Delete the socket from pollthread
pollthread_tc_5 Exercise listen/accept of TCP sockets in pollthread
Test creation of a listen pollthread
Test accept of socket via listen pollthread
Test message on the read-write socket

## Slide 27: UT Results
15 Jan 2015 CodeChix.org OFconnect
TEST: /home/libccof/deepa-git/OFconnect/tests/pollthr_test.exe... (pid=12123)
/pollthread/tc_1: OK
/pollthread/tc_2: OK
/pollthread/tc_3: OK
/pollthread/tc_4: OK
/pollthread/tc_5: OK
PASS: /home/libccof/deepa-git/OFconnect/tests/pollthr_test.exe
TEST: /home/libccof/deepa-git/OFconnect/tests/util_test.exe... (pid=12154)
/util/tc_1: OK
/util/tc_2: OK
PASS: /home/libccof/deepa-git/OFconnect/tests/util_test.exe
Notes: util_test.c
util_tc_1 Verify one rw pollthread and one listen pollthread via utility functions
Test creation of rw pollthread via utility function
Test creation of listen pollthread via ap_thr_mgr API
Test global rw_pollthread_list entry
util_tc_2 Exercise TCP NET_SVCS to create a tcp socket and receive message
Note: this test requires port 6633 to be available
Test API cc_of_dev_register with a receive function that prints the received text message
Simulate the client (switch) with its own rw pollthread and NET_SVCS TCP pollin/pollout functions
Test 'connect' to the server from the switch
Test addition of rw socket (of client's) to its rw pollthread: cc_add_sockfd_rw_pollthr_safe utility function
Test process_tcpfd_pollout_func for simulated switch by writing to client socket fd directly into the data pipe of the rw pollthread
Test receive of the message at server (controller)

## Slide 28: Next Up
Introduction
OFconnect Design
Unit Test Automation
Controller Integration
SDN Setup
Get Started!
15 Jan 2015 CodeChix.org OFconnect

## Slide 29: HOWTO Integrate OFconnect
Implement three API callbacks:
(*cc_of_accept_channel)()
(*cc_of_delete_channel)()
(*cc_of_recv_pkt)()
Controller/Switch process start/restart:
        cc_of_lib_init()
        cc_of_dev_register()
Controller/Switch cleanup:
        cc_of_dev_free()
        cc_of_lib_free()
15 Jan 2015 CodeChix.org OFconnect

## Slide 30: Next Up
Introduction
OFconnect Design
Unit Test Automation
Controller Integration
SDN Setup
Get Started!
15 Jan 2015 CodeChix.org OFconnect

## Slide 31: Test Setup
sudo mn --controller=remote, ip=127.0.0.1 --switch ovsk
Virtual Hosts
c0 MUL Controller
Port:6633
OFconnect Driver
15 Jan 2015 CodeChix.org OFconnect

## Slide 32: Wireshark Capture
18 Nov 2014 CodeChix.org OFConnect

## Slide 33: Looking Ahead
Enhance
TLS, IPv6
Greater OF Awareness
Scale
256K connections
Perform
Profile and Benchmark
15 Jan 2015 CodeChix.org OFconnect

## Slide 34: OFconnect Summary
Simple and powerful
True OpenFlow
Easy to integrate
GPL v2
15 Jan 2015 CodeChix.org OFconnect

## Slide 35: Next Up
Introduction
OFconnect Design
Unit Test Automation
Controller Integration
SDN Setup
Get Started!
15 Jan 2015 CodeChix.org OFconnect

## Slide 36: Join and Contribute!
Getting Started
      https://github.com/CodeChix-OpenSource/OFconnect/wiki
Prototype Controller
      https://github.com/codechix/mul-OFconnect
Email: organizers@codechix.org
15 Jan 2015 CodeChix.org OFconnect

## Slide 37
Thank you!
CodeChix Confidential Proprietary